## Slide 1: Practical Considerations
786

## Slide 2: Sample Preparation
Concentration
  Size does not depend on concentration
  Often there is a large concentration range that gives good results for any given sample
  When measuring a new sample: start with a stock solution, prepare several dilutions (on a log scale) and test before picking an optimal one
Sample turbidity
  Ideally want ‘single scattering’ events
  Turbid samples can be measured by DWS, back scattering

## Slide 3: Dust & Vibrations & Cleanliness
Dust
  The perfect size to scatter light
  Can adversely affect results
Vibrations
  Instrument has a built-in vibration damper
  Still: Do not place objects on top of box
  Avoid strong vibrations (e.g. hitting the table)
Clean Sample
  Filtered samples
  Cleaned Vials
Clean Solvent
  When measured should reveal “nothing”

## Slide 4: Angle of Measurement
Small particles scatter isotropically
Large particles preferentially scatter in the forward direction
Measurement at ~1500 (back scattering) can be used to observe small particles even when small numbers of larger ones are present
Particles less than ~10-20 nm

## Slide 6: Adjusting intensity
Consider both correlation function and amount of scattered light when judging data quality
Noisy data can be improved by:
  Increasing incident intensity
  Longer collection times
  Increasing concentration
Incident laser intensity
Number of “scatterers”
~ concentration